## Slide 1: Skeletal & Reduced Models for Cat A2, C1, C5 Yang Gao & Tianfeng Lu University of Connecticut Email: tianfeng.lu@uconn.edu

## Slide 2: Development of Fuel Specific Reduced Models
Detailed HyChem models
  Cat A2, C1 and C5
Methods (Lu & Law, PECS 2009)
  Directed Relation Graph (DRG)
  DRG-Aided Sensitivity Analysis (DRGASA)
  Removal of unimportant reactions
  Quasi Steady State Assumption (QSSA)
  Parameter range
  = 0.5-1.5, p = 0.5-30 atm, Tin = 300 K for PSR, T0 = 1000-1600 K for auto-ignition
  Results
  Validation targets
  Ignition delay, extinction of PSR and laminar flame speed
Models | Cat A2 | Cat C1 | Cat C5
Detailed HyChem | 119 | 119 | 119
Skeletal | 41 | 34 | 41
Reduced | 31 | 26 | 31

## Slide 3: Selected Validations in Auto-Ignition & Laminar Flame Speed
Solid lines : detailed HyChem model
Dashed lines : skeletal model
Symbols : reduced model
Blue : p = 0.5 atm
Red : p = 1 atm
Black : p = 5 atm
Magenta : p = 30 atm
Cat A2
Cat C1
Cat C5
Similar agreements for = 0.5 and = 1.5

## Slide 4: Changes in Year 1 & 2 Models
Detailed models:
    Fuel cracking reactions:
    Fuel + O reaction added as a cracking reaction (H, CH3, OH, O2, HO2, O)
    Cat A2: C4H8-1 added in cracked products
    Cat C1: C2H4 added in cracked products, removed aromatics (C6H6 C6H5CH3)
    Cat C5: C4H6 replaced by C4H8-1 in cracked products
    Oxidation core:
    Modified reactions for iC4H7 and iC4H8
    7 more species (CH*, OH*, HE, iC4H7-1, C2C*CC, C*C2CC, C8H14)
    Skeletal/Reduced models:
    Three more aromatics related species added to the skeletal models of A2 (C5H4O, C5H5, C3H3) and C1 (C5H4O, C5H5, c-C4H5) for better prediction of fuel rich conditions
Year 1 Cat A2 reduced vs. detailed
Year 2 Cat A2 reduced vs. detailed

## Slide 5: Next Steps
Validate the fuel specific reduced kinetic models in PSR at LBO conditions
Validate the fuel specific reduced kinetic models in counterflow extinction
Update the universal reduced kinetic model and universal reduced molecular diffusion model
Update/development of reduced sub-models for NO and PAH/soot

## Slide 6: Development of Reduced A2 Kinetic Model
Detailed HyChem model
  Cat A2 (POSF10325) with 119 species and 843 reactions
  Methods
  Skeletal reduction with DRG, sensitivity analysis and further removal of unimportant reactions
    Error tolerance in DRG and sensitivity analysis: 30%, 20%
    Error tolerance in removing unimportant reactions: 20%
    Targets in sensitivity analysis: auto-ignition delay, PSR extinction time
  Parameter space (auto-ignition and PSR)
  𝜙 = 0.5-1.5, p = 0.5-30 atm, Tin = 300 K for PSR, T0 = 1000-1600 K for auto-ignition
  Results
  Skeletal model: 41 species and 202 reactions
  Reduced model: 31 species

## Slide 7: Validations of Reduced Cat A2 Model
Solid lines : detailed HyChem A2 model (119 species)
Dashed lines: skeletal A2 model (41 species)
Symbols : reduced A2 model (31 species)
Blue : p = 0.5 atm
Red : p = 1 atm
Black : p = 5 atm
Magenta : p = 30 atm

## Slide 8: Development of Reduced C1 Kinetic Model
Detailed HyChem model
  Cat C1 (POSF11498) with 119 species and 843 reactions
  Methods
  Skeletal reduction with DRG, sensitivity analysis and further removal of unimportant reactions
    Error tolerance in DRG and sensitivity analysis: 30%
    Error tolerance in removing unimportant reactions: 20%
    Targets in sensitivity analysis: auto-ignition delay, PSR extinction time
  Parameter space (auto-ignition and PSR)
  𝜙 = 0.5-1.5, p = 0.5-30 atm, Tin = 300 K for PSR, T0 = 1000-1600 K for auto-ignition
  Results
  Skeletal model: 34 species and 182 reactions
  Reduced model: 26 species

## Slide 9: Validations of Reduced Cat C1 Model
Solid lines : detailed HyChem C1 model (119 species)
Dashed lines: skeletal C1 model (34 species)
Symbols : reduced C1 model (26 species)
Blue : p = 0.5 atm
Red : p = 1 atm
Black : p = 5 atm
Magenta : p = 30 atm

## Slide 10: Development of Reduced C5 Kinetic Model
Detailed HyChem model
  Cat C5 (POSF12345) with 119 species and 843 reactions
  Methods
  Skeletal reduction with DRG, sensitivity analysis and further removal of unimportant reactions
    Error tolerance in DRG and sensitivity analysis: 30%, 20%
    Error tolerance in removing unimportant reactions: 20%
    Targets in sensitivity analysis: auto-ignition delay, PSR extinction time
  Parameter space (auto-ignition and PSR)
  𝜙 = 0.5-1.5, p = 0.5-30 atm, Tin = 300 K for PSR, T0 = 1000-1600 K for auto-ignition
  Results
  Skeletal model: 41 species and 200 reactions
  Reduced model: 31 species

## Slide 11: Validations of Reduced Cat C5 Model
Solid lines : detailed HyChem C5 model (119 species)
Dashed lines: skeletal C5 model (41 species)
Symbols : reduced C5 model (31 species)
Blue : p = 0.5 atm
Red : p = 1 atm
Black : p = 5 atm
Magenta : p = 30 atm

## Slide 12: Laminar Flame Speed
Cat A2
Cat C1
Cat C5
Solid lines : detailed HyChem models
Dashed lines: skeletal models
Symbols : reduced models

## Slide 13: Non-Stiff Versions
Solid lines: SENKIN with implicit DASAC
Symbols: SENKIN with explicit RKF45, h = 10 ns
Dynamic stiffness removal (Lu et al., CNF 2009) enables explicit time integration with time step ~< 20ns, suitable for compressible flow simulations